## Slide 1: Front-end electronics developments for OPERA
C. de LA TAILLE, G. MARTIN-CHASSARD, L. RAUX
LAL Orsay
T.D. LE, P. SCHMITT
IRES Strasbourg
http::/www.lal.in2p3.fr/technique/se/opera

## Slide 2: Variable gain preamp for PMT
Common base architecture
  Fast current integrator : Vout/Iin = Rf/(1+ sRfCf)
  Low input impedance (1/gm=250 ) -> crosstalk reduction
  Gain variation by changing Cf from10 pF to 45 pF (3 bits) -> can easily be extended
  Decay time kept constant (RfCf = 200 ns) by also switching resistors
VDD
VSS
C line
I in
Sw R1
Sw R2
Sw R3
Sw C3
Sw C1
Sw C2
10p
20p
5p
10p
Slow out
Fast out
VDD
20K
40K
10K
20K
20K

## Slide 3: Variable gain preamp for PMT
Current mirror architecture
  Ratioed mirrors on input. Output currents summed and integrated on capacitor (10 pF)
  Gain adjusted by turning on/off scaled mirrors (3 bits).
  Larger input impedance (500 ), similar decay time constant (200 ns)
  Same following stages.
I in
10p
VDD
VDD
VDD
VSS
2K
2K
20K
cmd1
cmd1
cmd2
cmd2
cmd3
cmd3
1200µ
2µ
1200µ
2µ
300µ
0.8µ
300µ
0.8µ
600µ
2µ
300µ
0.8µ
400µ
2µ
300µ
0.8µ
300µ
2µ
300µ
0.8µ
C line

## Slide 4: Fast and slow shapers
Simple CR RC architecture
  Slow shaper : t = 100 ns G ~ 1
  Fast shaper : t = 10 ns G ~ 20
  Return current taken from integrating capacitor -> area reduction
Preamp.
Slow
Shaper
Fast
Shaper
10p
10K
1p
100K
100K
100f
Rp
Cp
VDD
IN
Charge Output
Trigger Output
Preamplifier block

## Slide 5: Current mirror performance
Fully functional
  Gain adjustment : 1.25*1.33*1.5 = 2.5
  Slow shaper : tp = 60 ns G = 34 mV/p.e. rms noise : 600 µV ; S/N = 66
  Fast shaper : tp = 12 ns G = 208 mV/p.e.
  Linearity : ± 1% up to 80 photoelectrons. Dynamic range : 5000 = 12 bits
1 MIP = 6 p.e.
Slow shaper : Residuals of linear fit
± 0.5 %
1/2 photelectron

## Slide 6: Common base performance
Fully functional
  Oscillations between neighbours : 100  necessary in emitters
  Gain adjustment : 1-4.5
  Fast and slow shaper similar to current mirror version.
  Linearity : ± 1% up to 90 photoelectrons. Dynamic range : 10000
Slow shaper : Residuals of linear fit
± 0.5 %
Preamp output

## Slide 7: Noise performance
Noise in photoelectrons with variable shaper
  Better performance at fast shaping for the common base
  Noise dominated by parallel noise

## Slide 8: Front-end chip for HPD
Complete front-end chip, 16 inputs, 1 trigger + 1 multiplexed output
  low noise charge preamplifier (Cf = 0.25 pF)
  Fast shaper (75ns) for auto-trigger
  Slow shaper (500 ns) for accurate charge measurement (minimum noise)
  On chip track and hold and output multiplexer

## Slide 9: Measurement results (I)
Preamplifier
  Test channel with preamp output accessible, followed by variable shaper
  Preamplifier gain : 1.8 mV/p.e. (1 p.e. = 3000 e-)
  Rise time : tr = 90 ns
  Good agreement with simulation, except for noise
Preamp output Qin=10 p.e.

## Slide 10: Noise measurements
HPD preamp (2000/0.8 PMOS)
  ID = 0.5 mA, gm = 7.1 mA/V, en = 1.7 nV/√Hz, Ca = 8 pF, ENC(75ns,6pF)=550 e-
  Significant gate resistance (RG ~ 80 ). and substrate resistance noise contribution
ATLAS 10 000/0.8 AMS PMOS transistor :
  ID = 0.5 mA, gm = 8 mA/V, en = 1.0 nV/√Hz, Ca = 21 pF
  Minimum gate resistance (RG ~ 2 ) and substrate resistance noise contribution
HPD preamp
10000/0.8 PMOS

## Slide 11: Noise improvement
New layout for ~50% noise improvement
  Size : 2000/0.8 similar transconductance (7 mA/V) with smaller capacitance (8 pF)
  Different geometry to minimize gate resistance (RG : 80 → 2 ).
  Bias substrate positively (VBS = +2V) to mimimize substrate noise contribution
  Target : en = 1.0 nV/√Hz, Ca = 8 pF at ID = 0.5 mA
Current design : (Cd = 6 pF)
ENC = 550 e- @ tp = 75 ns
ENC = 300 e- @ tp = 500 ns
Goal : (with Cd = 6 pF)
ENC = 300 e- @ tp = 75 ns
ENC = 150 e- @ tp = 500 ns
  Capacitance breakdown :
    PMOS : 2.5 pF
    input pads : 0.8 pF
    Cf+Cinj : 0.5 pF
    package : 1 pF
    PCB : 2.4 pF

## Slide 12: Measurement results (II)
Slow shaper
  tp = 500 ns G = 2.7 mV/photoelectron
  Linearity : ± 0.5 % up to 300 photoelectrons
Fast shaper
  Coupling with preamp inputs -> oscillations
  Could only be measured separately
Slow shaper : Residuals of linear fit
± 0.5 %
Slow shaper Qin=10p.e.
Fast shaper Qin=10p.e.

## Slide 13: Measurement results (III)
Track and hold
  All channels functional
  Pedestal variation : ~ 100 mV : to be improved
  Output multiplexer : OK
Discriminator
  Low offset design
  Not yet tested

## Slide 14: Conclusion
PMT chips
  Both designs fully functional
  Lower noise with common base but more robust design with current mirrors
  Good noise (~ 0.01 p.e.), linearity in ± 1% up to ~ 100 photoelectrons
  Fast trigger output (12 ns)
HPD chip
  Only partially functional (oscillations in fast shaper)
  Noise : 550e- = 0.2 p.e. at tp = 75 ns, Cd = 6pF ; 300e- at tp = 500 ns
  Preamp noise can be decreased by 50%, down to 1.0 nV/√Hz or 300 e- at tp = 75 ns
  Linear within ± 0.5% up to ~ 300 photoelectrons
Ready for one iteration
  After detector selection
  Full scale prototype ?