## Slide 1
GDR-Neutrino (10-11 mai 2006)
L. Mosca (CEA-Saclay)
The MEMPHYS project
(Laboratory excavation)
  MEgaton Mass PHYSics
in a Large
International Underground Laboratory
in the Fréjus tunnel
- proton decay
- supernovae explosion
- solar and atmosphéric neutrinos
- neutrino super-beam and beta-beam from CERN

## Slide 2: Physics Motivations
Nucleon Decay
Super Novae Neutrinos:
  burst & relic
Solar & Atmospheric Neutrinos
Neutrinos from Accelerators
  Super Beam, Beta Beam
And also:
  Dark Matter (WIMP) indirect detection, High energy neutrinos,…

## Slide 3: The MEMPHYS Project
65m
65m
Fréjus
CERN
130km
4800mwe
Excavation engineering pre-study has been done for 5 shafts
Water Cerenkov modules at Fréjus
CERN to Fréjus
Neutrino Super-beam and Beta-beam

## Slide 5: « Convergence » measurements along the Fréjus road tunnel

## Slide 6: A Very Large Laboratory
In the middle of the Fréjus tunnel at a depth of4800 m.w.e
a preliminary investigation shows the feasibility to excavate up to five shafts of about 250,000 m3 each

## Slide 7
Main results of the Preliminary Study
1) the best site (rock quality) is found in the middle of the mountain,
at a depth of 4800 mwe : a really good chance !
2) of the two considered shapes : “tunnel” and “shaft”,
the “shaft (= well) shape” is strongly preferred
3) Cylindrical shafts are feasible up to :
a diameter  = 65 m and a full height h = 80 m (≈ 250 000 m3)
4) with “egg shape” or “intermediate shape” the volume
of the shafts could be still increased
5) The estimated cost is ≈ 80 M€ X Nb of shafts

## Slide 8
Exemple of “egg shape” simulation, constrained by the rock parameter measurements made during the present tunnel and laboratory excavation.
The main feasibility criterium is that the significantly perturbated region around the cavity should not exceed a thickness of about 10 m

## Slide 10
Two examples of scenario for Water Cerenkov detectors
a) 3 shafts of 250 000 m3 each, with a fiducial mass of 450 Ktons
(“UNO-like” scenario)
b) 4 shafts of 250 000 m3 each, with a fiducial mass of 600 Ktons
_____________________________________________________
-> In both scenarios one additional shaft would be necessary for
a Liquid Argon detector of about 100 ktons total mass

## Slide 11: A MegaTon scale Detector
3 to 4 Water Cerenkov modules ( = 20 x Super K
≈ 500kT fiducial mass) equipped with a large number of Photodetectors (eg. 250,000 PMTs 12”)
a very well proved and robust technique which provided already remarkable physical results mainly in Nucleon Decay and Neutrino Physics and Astrophysics

## Slide 12: Very intense 300÷400 MeV Neutrino Beams from CERN
Super Beam based on a 4MW Proton Driver (eg. SPL) :
and  from pion decay
Beta Beam (possibly in connection with the EURISOL project) :
eand e from heavy ions decay

## Slide 13
SUPERBEAM BETABEAM
 → e e → 
 → e e → 

Superbeam + beta beam together
2 ways of testing CP, T and CPT : redundancy and check of systematics
2 beams
1 detector
2yrs
8yrs
5yrs
5yrs
pure
4  flavours + K


## Slide 14
A possible schedule for a European Lab. at Frejus
Year 2005 2010 2015 2020
Safety tunnel
Excavation
Lab cavity
Excavation
P.S
Study
detector
PM R&D
PMT production
Det.preparation
Installation
Outside lab.
Non-acc.physics
P-decay, SN
Superbeam
Construction
Superbeam
betabeam
Beta beam
Construction
decision for cavity digging decision for SPL construction decision for EURISOL site

## Slide 15
La “saga” du tunnel routier de sécurité du Fréjus :
diamètre du tunnel
date partie Française partie Italienne
mars 2001 0.00 (zero) m 9.50 m
décembre 2001 4.80 m
juin 2004 5.50 m
2 juillet 2004 : création d’un groupe de travail à ce sujet par les deux
ministres de l’équipement/transports :
Français (Gilles de Robien) e Italien (Pietro Lunardi).
Cette Commission devait rendre son rapport pour
le 31 Octobre 2004
septembre 2004 5.50 m 8.30 m
mars 2006 8.20m
(Comité de Sécurité Franco-Italien)
21 avril 2006 8.00 mètres “utiles”
(Commission Inter-Gouvernementale Franco-Italienne)