## Slide 1: SPL-based Proton Driver for  Facilities at CERN: Updated Description
C.R. Prior for
R. Garoby, F. Gerigk and the SPL study group
ISS meeting, 23-25.1.06

## Slide 2: Outline
Re-design of the SPL
Applications
Staged construction
SPL beam characteristics
Scenarios for accumulation and compression
Conclusions & outlook

## Slide 3: 1. Re-design of the SPL (2005/6)
352.2 MHz LEP RF equipment
SC cavities, 1MW CW klystrons
CERN neutrino factory design
2.2 GeV target
progress in bulk Nb SC technology
4x accel.grad., pulsed 4-5 MW klystrons
designed for multiple users
-beam, superbeam, , EURISOL, PS II
SPL CDR1
2000
SPL CDR2
2006
SC technology has progressed a lot
Optimum energy is higher

## Slide 4
SC linac replacing the 40 years old PS booster (1.4 GeV)
5 MW driver for EURISOL
[0.2 – 5 MW beam @ 1-2 GeV]
-  factory based on  decay
[4 MW @ 4 - 10 GeV]
LHC upgrade
[proton beams with
 2x brightness]
 facility based on:
Major upgrade of the proton injector complex at CERN [ performance:  2x higher brightness + reliability] for the benefit of all users (LHC, fixed target etc.)
 Cost-effective time sharing between nuclear [ISOL] and  applications
 Potential for future increases in energy and/or power
2. Applications
beta-beam [200 kW beam @ 1-5 GeV]
+
super-beam
or

## Slide 5: 3 MeV test stand (beam in 2008)
buncher cavity
chopper in quadrupole
IPHI RFQ (CEA)
halo monitor
3. Staged construction (1/5)

## Slide 6
Linac4 (beam in 2010)
ITEP Moscow & VNIIEF Sarov
& IN2P3
BINP Novosibirsk &
VNIITEF Snezinsk
IN2P3, BINP, CEA, VNIITEF
low duty cycle: 0.08%
3. Staged construction (2/5)

## Slide 7
SPL (beam in 2015 ?)
relocation of Linac4, adding 366 m of SC RF,
PS booster becomes obsolete,
cavity power < 1 MW,
TESLA/ILC type cryostats (INFN Milano) with
5-cell SC Nb cavities (CEA/INFN) and cold
quadrupoles,
layout and beam dynamics (CEA Saclay).
3. Staged construction (3/5)

## Slide 8
3. Staged construction (4/5)

## Slide 9: Beam dynamics (CEA Saclay)
phase advance per metre
emittance evolution
beam envelopes
output phase space
3. Staged construction (5/5)

## Slide 10
 | CDR1 [2000] | CDR2 [2006] | 
energy | 2.2 | 3.5 | GeV
average beam power | 4 | 4 | MW
length | 690 | 450 | m
average RF power | 24 | 17.4 | MW
average cryogenics power | 9.6 | 6.7 | MW
repetition rate | 50 | 50 | Hz
beam pulse length | 2.8 | 0.57 | ms
average pulse current* | 13 | 40 | mA
peak current* | 20.8 | 64 | mA
beam duty cycle | 14 | 2.9 | %
peak RF power | 32 | 163 | MW
no. of 352.2 MHz klystrons (1 MW) | 44 | 14 | 
no. of 704.4 MHz klystrons (5 MW) | - | 44 | 
no. of tetrodes | 79 | 3 | 
cryo temperature | 4.5 | 2 | K
* after chopping
4. SPL beam characteristics

## Slide 11
5. Scenarios for accumulation & compression (1/7)
- for a beta-beam based facility
[200 kW beam @ 1-5 GeV]
+
super-beam [4 MW @ 3.5 GeV]
Long beam burst (~ms)
direct use of linac beam
- for a  factory [4 MW beam @ 4-10 GeV]
Short beam burst (~s)
accumulator
Short beam burst (~s)
accumulator
+
Short bunches (~ns)
compressor
For  physics, the time structure of the linac beam has to be changed:
The requirements of a  factory are the most demanding.

## Slide 12
5. Scenarios for accumulation & compression (2/7)
Beam power (P) | ~ 4 MW
Kinetic energy (T) | 4 – 10 GeV
Bunch length | 1-2 ns rms
Distance between bunches | 100 ns
Burst length | 1-3 s
Repetition rate | 50 Hz
Parameters required by a  factory*
* As estimated today

## Slide 13
5. Scenarios for accumulation & compression (3/7)
Consequences for a linac-based driver
Kinetic energy (T) | Cost increases with T  Minimize T (< 4 – 8 ? GeV)
Repetition rate (frep) | Constraints to a minimum number of protons/pulse Np
Bunch length (lb) | Energy acceptance + longitudinal space charge restrict to low longitudinal emittance  minimum number of bunches (Nb)
Distance between bunches (db) | Accumulator circumference C is proportional to Nb  db & Laslett tune shift Q is proportional to C  minimize db to minimize Q & cost
Burst length | Constraints the highest value of C

## Slide 14
5. Scenarios for accumulation & compression (4/7)
With SPL CDR1 (2000): severe constraint due to the low beam energy
T | 2.2 Gev
frep | 50 Hz
Np | 2.27 1014
lb | 1 ns
Nb | 140
db | 22.7 ns
C | 3.316 s

## Slide 15
5. Scenarios for accumulation & compression (5/7)
With SPL CDR2 (2006): higher beam energy => less constraints
Kinetic energy (T) | 3.5 GeV
Repetition rate (frep) | 50 Hz  Np= 1.43 1014 p/p
Bunch length (lb) | For the same p/p acceptance + because of lower Np + relaxing on lb (2 ns instead of 1 ns)  Nb (goal) = 17 [8.41 1012 p/b]
Distance between bunches (db) | db (goal) = 90.86 ns C (goal) = 1.635 s
Aggressive approach…
Study is going on to check feasibility…

## Slide 16
5. Scenarios for accumulation & compression (6/7)
With a linac-based driver there is the possibility to do multiple accumulations with a single linac beam pulse, and therefore generate multiple bursts of beam onto the target.
This is of interest if:
all parameters are constant in the  channel during the whole duration of the proton beam on the target (transverse focusing, gradient in the RF cavities…). It is not unreasonable to hope for ~ 1 ms.
the  storage ring is long enough to contain all the successive bursts.
The main disadvantage is that the kickers must provide multiple kicks within ~ 1 ms.
This makes it possible to tailor the intensity per burst / the distance between bunches / the main cycling rate of whole facility…

## Slide 17
5. Scenarios for accumulation & compression (7/7)
With SPL CDR2 (2006): other approach using multi-pulsing
Kinetic energy (T) | 3.5 GeV | 3.5 GeV
Repetition rate (frep) | 50 Hz  Np=2  0.72 1014 p/p | 25 Hz  Np=2  1.43 1014 p/p
Time interval between pulses | 0.285 ms | 0.570 ms
Bunch length (lb) | Nb = 17 [4.21 1012 p/b] | Nb = 17 [8.41 1012 p/b]
Distance between bunches (db) | db = 90.86 ns C = 1.635 s | db = 90.86 ns C = 1.635 s
If the first set of parameters
is unfeasible: pulse twice
the accumulator/compressor
If the first set of parameters
is feasible: pulse twice
the accumulator/compressor
and divide frep by 2

## Slide 18
The new SPL design (CDR2 – 2006) is largely improved:
energy (3.5 GeV) is a compromise that can potentially satisfy EURISOL, neutrino applications, and LHC upgrade scenarios,
design is more optimum (length reduced by 35% while the energy is increased by 60%, higher instantaneous current reducing the number of turns for accumulation in the ring…)
upgrades are possible in terms of energy and/or power.
This typically illustrates the potential of a linac-based proton driver for a  factory, which has an unmatchable flexibility to adapt to the requirements of the following part of the facility.
6. Conclusions & outlook