## Slide 1: Large area photodetection for Water Cerenkov detectors PMm2 proposal: Front End Electronics MAROC ASIC
Pierre BARRILLON, Sylvie BLIN, Jean-Eric CAMPAGNE, Christophe de LA TAILLE, Nathalie SEGUIN-MOREAU
(LAL ORSAY)
Joel POUTHAS, Bernard GENOLINI
(IPNO IN2P3)

## Slide 2: Large area photodetection requirements
Single photoelectron sensitivity
Excellent time resolution ~100 ps
High granularity
Scalability
Low cost
Profit from progress in micro-electronics and DAQ !
Many issues in common with HPD or large PMs developments by KEK

## Slide 3
Joël Pouthas IPN Orsay
Integrated electronics (Multichannel, close to the PMTs)
“PMm2” (2006 – 2009), funded by the ANR (National Agency for Research)
  LAL Orsay, IPN Orsay, LAPP Annecy and Photonis
  Replace large PMTs (20”) by groups of smaller ones (12”)
  Use central multi-channel ASIC (MAROC)
  Use common High Voltage to reduce cost
  Only one wire out (DATA + VCC)
  Water-tight
  Target low cost
R&D PROGRAM FOR PMm2
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: MAROC : 64 ch MAPMT chip for ATLAS lumi
PMTs : 5x5 array of 64 anodes PMT
few external components
3*3 cm2
Chip On Board
MAROC1
BOTTOM side
2x10x16
Appareillage

## Slide 5: MAROC : 64 ch MAPMT chip for ATLAS lumi
  Similar to OPERA ROC
  Low input impedance (50-100 Ω)
  6 bits gain adjustment (G=0-4) per channel
  64 discriminator outputs
  100% sensitivity to 1/3 photoelectron (50fC). Counting rate up to 2 MHz
  Common threshold loaded by internal 10bit DAC (step 3mV)
  1 multiplexed charge output with variable shaping 20-200ns and Track & Hold.
  Dynamic range : 11 bits (2fC - 5 pC)
  Crosstalk < 1%
Hold signal
Photomultiplier
64 channels
Photons
Variabl
Gain
Preamp.
Variable
Slow Shaper
20-100 ns
S&H
Bipolar
Fast Shaper
Unipolar
Fast Shaper
Gain correction
64*6bits
3 discri thresholds (3*12 bits)
Multiplexed
Analog charge output
LUCID
S&H
3 DACs
12 bits
80 MHz encoder
64 Wilkinson 12 bit ADC
64 trigger outputs (to FPGA)
Multiplexed
Digital charge output
64 inputs

## Slide 6
64 channels
  Preamps
  Fast shaper 15ns
  Discriminators
  Slow shaper
  Track&Hold
  12bit ADC
  10bit DAC
  Bangap reference
  Digital formatting
Silicon Germanium
  0.35µm BiCMOS
  16mm2 area

## Slide 7: MAROC performance

## Slide 8: ADC performance
Wilkinson type
64 channels
12 bits
80 µs conversion time

## Slide 9: CONCLUSION
MAROC2 fullfills most of the requirements of 2 km WC
  Chip mature, used in ATLAS luminometry
To be done:
  Time dizitization (100 psTDC)
  Data out “on power wire”
  Test on a prototype (16 PMs, 8’’) with MAROC2 foreseen shortly at IPNO
Joint activities with KEK :
  Tests at KEK by Tanaka-san
  Common ASIC development : TDC, ADC, DAQ,
  Specific preamp for HPD
  Characterization of common parts

## Slide 10: TEST BOARD
MAROC (COB)
64ch PM socket
USB port
GPIB port
Control Altera
Notes: <number>
<footer>
<header>
<date/time>
You can see the test board with chip on board
The oscillation problem have been almost solved by chip on board
There are no longer oscillations at gain lower than 2