## Slide 1: MEMPHYNO
Simulation studies for the prototype of MEMPHYS detector
Alessandra Tonazzo/APC
Nikos Vassilopoulos/LAL

## Slide 2: MEMPHYNO simulation parameters
MEMPHYS, underwater cherenkov detector simulation & visualization code by Jean-Eric Campagne, Guy Barrand et al. (based on GEANT4)
2x2x2m³ water volume
2 different PMTs’ modules simulated at bottom side:
    4x4 12in PMTs =
        ~35% coverage (for one side, shown here)
    4x4 10in PMTs =
        ~20% coverage (for one side, available)
water refraction & blacksheet parameters a la SK
MEMPHYNO detector display

## Slide 3: MEMPHYNO detector visualization
electron 10 MeV, pz / p = -1, vtx : centre
muon 1 GeV, pz / p = -1, vtx : top centre
shots taken only for optical photons detected

## Slide 4: MEMPHYNO event reconstruction
particles generated (10k events samples per particle per energy) :
    electrons: E = 1 to 25 MeV
     point-like sources deployed at the detector centre
    muons: E = 1 GeV, pz/p = -1 (also pz/p < 0)
     downward selected muons
plots of the following event (particle) characteristics:
    # of PMTs per electron
    # of opticalphotons per PMT
    opticalphotons’ arrival times at PMTs
preliminary analyses for vertex reconstruction & light propagation

## Slide 5: MEMPHYNO electrons 1 to 25 MeV
# of PMTs per electron :
blacksheet reflective
7x10k electrons generated at the detector’s centre with random direction

## Slide 6
MEMPHYNO
electrons 1 to 25 MeV
# of opticalphotons per PMT :
blacksheet reflective
7x10k electrons generated at the detector’s centre with random direction

## Slide 7
MEMPHYNO
electrons 1 to 25 MeV
opticalphotons’ arrival times :
blacksheet reflective
7x10k electrons generated at the detector’s centre with random direction

## Slide 8
MEMPHYNO
electrons 1 to 25 MeV
  average values of
    # of PMTs per electron
    OPs’ per PMT
    OPs’ arrival times
  plots for
    blacksheet reflective a la SK
    blacksheet 100% absorption
el E (MeV) | 1 | 2.5 | 5 | 10 | 15 | 20 | 25
OP / MeV / el | 0.2 | 1.1 | 1.5 | 1.7 | 1.8 | 1.8 | 1.8
X 6 (sides) | 1.2 | 6.6 | 9 | 10.2 | 10.8 | 10.8 | 10.8
MEMPHYS | 2 | 7.7 | 10 | 10.9 | 11.1 | 11.2 | 11.1
  Table: MEMPHYNO’s OPs detected per MeV per electron with blacksheet reflective (numbers calculated from the total # of OPs per Energy run not from the averages)
7x10k electrons generated at the detector’s centre with random direction
similar to MEMPHYS

## Slide 9: MEMPHYNO electrons 10 MeV : vertex finding
primary vertex fit based on each PMT’s timing info: ti PMT = ti + TOFi => ti = ti PMT – TOFi
, where TOFi = (n / c) x D, D = distance between each PMT and fitting point’s coordinates
maximize estimator E(ti) to find the true vertex of electron :
blacksheet reflective
80 % reconstruction efficiency exactly
on true vertex for 10k electrons generated at the
detector’s centre with random direction.
for best fit
for best fit
for best fit
for best fit

## Slide 10: MEMPHYNO muons 1 GeV
# of PMTs per muon, # of opticalphotons per PMT, opticalphotons’ arrival times :
blacksheet reflective
blacksheet reflectivity=0
10k muons generated at the detector’s surface with pz / p = -1

## Slide 11: MEMPHYNO muons 1 GeV
light propagation effect of OPs :
plots of distance between muon’s exit point and detection PMT’s coordinates versus detection time
pz/p = -1
pz/p = -1
pz/p = -1
pz/p < 0
pz/p = -1 : later produced OPs are detected first
pz/p < 0 : relation not clean
blacksheet reflective
entry/exit: edges
entry/exit: middle
diagonal
trajectory
entry/exit: centre

## Slide 12: MEMPHYNO further simulation work
on-going :
  design of larger/different configurations for MEMPHYNO (summer student working on this at APC) :
future :
  analyses of different electrons samples & new configurations
  inclusion of noise and digitization

## Slide 13: MEMPHYNO conclusions
a detector prototype, similar to a MEMPHYS module, is going to provide a solid platform to perform tests on electronics :
    DAQ
    self triggering
    threshold studies
analyses, as far as detector characteristics allow, could be performed for :
    vertex finding
    light propagation