## Slide 1: Large Format PMTs from Hamamatsu Photonics
Next Generation of Nucleon Decay
and Neutrino Detectors
Hamamatsu Photonics France
Alex Birkel
<Contents>
What is Hamamatsu Photonics ??
Large Format Photomultiplier
Notes: Thank you for inviting our company to this Workshop.
My name is Yuji Yoshizawa. I’m from Hamamatsu Photonics Electron tube center. I’m in charge of technical support for PMT in scintillation application, especially for HEP experiment. I will talk about Recent Development in Vacuum Devices.
First, I will briefly explain you What Hamamatsu Photonics is. Then, I will show you latest trend of development and large format detector.

## Slide 2: Where is Hamamatsu Photonics ?
Hamamatsu City
(Industrial city)
Hamamatsu is a name of a city.
HONDA, YAMAHA and SUZUKI
(famous motor cycle companies)
are located in the same area.
Population : 600K
Notes: Where is Hamamatsu Photonics ?
Hamamatsu is a name of a city. It’s located just between Tokyo and Osaka.
HONDA, YAMAHA and SUZUKI, these are famous motor cycle companies, which are located in the same area. So Hamamatsu is an industrial city. Its population is about 600K. When we have sunny day, we can see Mount Fuji from there.

## Slide 3: Hamamatsu Photonics
Established :
Sept 29, 1953
Net Sales : (2004)
62,245M yen
Employees : 2,500
(As of Sept. 2004)
Electron Tube Center
Solid Sate Division
System Division
Laser Group
Central Research Lab
Notes: Hamamatsu Photonics was established in 1953, net sales of last year was about 500M dollar, number of employees is about 22 hundreds.
We have 4 production divisions. These are Solid State Division, Electron Tube Center, System Division and Laser Group. We also have Central Research Laboratory.
1. Solid State Division makes Opto-Semiconductors. Main products are Silicon PhotoDiodes, APD and Image Sensors.
2. Electron Tube Center (other slides)
3. System division makes streak camera, high resolution digital camera, oxygen monitor for premature baby and so on. This picture shows body line scanner, which is used for research purpose.
4. Laser group makes High Power Laser diode, which is used for material process and maybe Laser fusion in near future.
5. CRL (another slide)

## Slide 4: Electron Tube Center
Notes: Electron Tube Center has these technology. Vacuum, Material Processing, Glass Fabrication and Electron-Optics Design. Based on these technology, products are made.

## Slide 5
Products of the Electron Tube Center
PMT’s
PMT Modules
Image Intensifiers
Ion Detectors
Fiber Optic Plates
with Scintillator’s
UV Spot Light Sources
Microfocus X-Ray
Sources
X-Ray Image
Intensifiers
Scientific
Light Sources
Notes: Major products are PMTs and Modules, Image Intensifiers, Ion Detectors, X-ray Image Intensifiers, Microfocus X-ray Sources, Fiber Optic Plates with Scintillators, Scientific Light Sources and UV Spot Light Sources.

## Slide 6: Large Format PMTs for Neutrino Experiments
Large Format PMT Lineup
Notes: Next topics is large format PMTs for neutrino experiments. This picture shows Large Format PMT Lineup. I will explain you about examples of neutrino experiments, which use these PMTs.

## Slide 7: R5912 (8 inch) R5912-02 (14-ST)
Improved type
of former R1408
Notes: At first, 8 inch PMT. This is R5912, its improved type of former R1408.

## Slide 8: SNO at Sudbury/Canada
Heavy Water (1000 ton)
in 12 m acrylic vessel
(NaCl is included)
Solar Neutrino Experiment
Pure Water
9,600 pcs of R1408
30 m
Solar neutrino = 66 billion/cm2・sec
Solar neutrino = Electron neutrino
Notes: This is a sketch of SNO experiment at Sudbury in Canada. This is solar neutrino experiment, and it uses 9,600 pcs of R1408. 1,000 ton of heavy water is set inside of this 12 m acrylic vessel, it contains NaCl. PMTs are attached to this cage, and are looking to this acrylic vessel. Pure water is filled in this external tank for supporting this vessel. As you know, SNO found that solar neutrino, which is electron neutrino coming from sun, is 2/3 of expectation. It indicates that neutrino has oscillation.

## Slide 9: MILAGRO at LANL/USA
Research for VHE gamma ray
with its direction and energy
< Location >
The Jemez Mountains
near Los Alamos
New Mexico/USA
R5912
VHE gamma
=> Shower in air
=> Cherenkov
Large water pond
Notes: This is a sketch of MILAGRO experiment. It’s located in the Jemez mountains near Los Alamos in New Mexico. The purpose is research for VHE gamma ray while detecting its direction and energy. About 800 pcs of R5912 are set in a large water pool to see Cherenkov light produced by VHE gamma ray. Precisely speaking, this is not neutrino experiment though.

## Slide 10: R7081 (10 inch) R7081-20 (14-ST)
Fits for 13 inch
Glass Sphere
Notes: Next is 10 inch PMT, R7081.

## Slide 11: ICECUBE at the South Pole
the South Pole
AMANDA
ICECUBE
Planned Location 1 km east
Skyway
Dome
R7081-02 is a candidate PMT.
IceCube is based upon work supported by the United States National Science Foundation under Grant Nos. OPP-9980474 (AMANDA) and OPP-0236449 (IceCube), University of Wisconsin-Madison.
Notes: This is South-pole again. This sketch shows location of experiments. AMANDA is here, and ICECUBE is 1 km east from here. R7081-02 is a candidate PMT.

## Slide 12: ICECUBE at South Pole
R7081-02
1500m
2000m
Notes: This is a sketch of AMANDA experiment at South-Pole. I think that there are some members of AMANDA experiment in this workshop, I don’t comment about the experiment so much, but I show its overview. About 800 pcs of R5912-02 are set below 1500 m in the ice. This is for detecting high energy neutrino coming from universe. Right now, it works well and ICECUBE experiment as its upgrade is under going.

## Slide 13: ANTARES at Marseille in the Mediterranean Sea
R7081-20
0.1Km2 as prototype
Notes: This is ANTARES experiment. Again, I think that there are some members of ANTARES experiment in this workshop, I don’t comment about the experiment so much, but I show its overview. The location is in front of Marseille in the Mediterranean Sea. 900 pcs of R7081-20 are used for 0.1Km2 as prototype of ANTARES experiment.

## Slide 14: R8055 (13 inch)
Fits for 17 inch
Glass Sphere
Notes: This is 13 inch PMT, R8055. Prime feature of this PMT is short length while using metal stem flange. It can be set inside 17 inch glass sphere.

## Slide 15: NESTOR at Pilos/Greece in the Mediterranean Sea
R8055 (2 tubes)
Notes: This is a sketch of NESTOR experiment. As there are some members of NESTOR experiment in this workshop, I don’t comment about the experiment so much. Its location is at PILOS/Greece in Mediterranean sea. It’s nice place and food is also very good. Its prototype was installed in March 2003, and is taking data right now.

## Slide 16: R3600-02 (20 inch)
Notes: This is 20 inch PMT, R3600-02. It’s the largest PMT in the world.

## Slide 17: SUPER-KAMIOKANDE Kamioka mine in Japan
20 inch PMT
(11,200 pcs)
42 m
40 m
ν
e-
=>
e-
Atmospheric neutrino
Muon neutrino => Tau neutrino
<Purpose>
Neutrino Astronomy
Neutrino Oscillation
Proton Decay
Notes: This is a sketch of SUPER-KAMIOKANDE experiment at KAMIOKA mine in Japan. The size of water tank is 40 m in diameter and 42 m in height. 11,200 pcs of 20 inch PMT are set inside the tank. 2,000 pcs of 8 inch PMT are also used for anti-counter. The purpose of this experiment are Neutrino Astronomy, Neutrino Oscillation and Proton Decay. As you know, it found Neutrino Oscillation with atmospheric neutrino in 1998. K2K experiment is going. Neutrino beam from KEK to Kamioka is used.

## Slide 18: SUPER-KAMIOKANDE Kamioka mine in Japan
Boat
Notes: This is a picture inside of the SUPER KAMIOKANDE. Some stuff are checking PMTs on a boat.

## Slide 19: R7250 (20 inch)
New electrode
for fast timing.
Effective area
is 17 inch.
Notes: The last one is new 20 inch PMT, R7250. It has new electrode, Box and Grid dynode, for fast timing. Effective area is limited as 17 inch.

## Slide 20: KamLAND at Kamioka mine in Japan
Liq. Scintillator (1000 ton)
in 13 m dia. Balloon
Stainless Steel Tank
with 1,330 pcs R7250
and 550 pcs of R3600
Pure water with
250 pcs of R3600
Detection of neutrinos come
from Nuclear Power Plants
anti-electron neutrino
Notes: This is a sketch of KamLand experiment at Kamioka mine in Japan. The purpose is detecting of neutrinos coming from Nuclear Power Plants. It consists of Liq. Scintillator in 13 m diameter balloon. Stainless steel tank is used for supporting it. Pure water tank is used as VETO counter. Total of more than 2,000 pcs of 20 inch PMTs are used.

## Slide 21: SUMMARY
< Type numbers and Examples of Experiments >
8 inch R1408 : SNO / CANADA, LSND / LANL
R5912 : MILAGRO / LANL, mini-Boone / FNAL
R5912-02 : AMANDA / South-Pole
10 inch R7081-02 : ICECUBE / South-Pole
R7081-20 : ANTARES (0.1km2) / Marseille
13 inch R8055 : NESTOR / Pilos/Greece
20 inch R7250 : KamLAND / Japan
R3600-02 : SUPER-KAMIOKANDE / Japan
?? Inch XXXX : KM3 EXPERIMENT
?? Inch XXXX : Other New Experiments
Notes: This is summary of Neutrino experiments. We are expecting that ICECUBE would use our R7081-02 and KM3 experiment will select one of our photodetectors.
My presentation is over, thank you for your attention.