## Slide 1: Overview of Hyper-Kamiokande R&D
Kenzo NAKAMURA
KEK
April 7-9, 2005
NNN05
Aussois, Savoie, France

## Slide 2: Mton Water Cherenkov Detector
Concept of a Mton water Cherenkov detector dates back to 1992
  M. Koshiba: “DOUGHNUTS”
  Phys. Rep. 220 (1992) 229
Concept of Hyper-Kamiokande was first presented at NNN99 @ SUNY
A recent write-up:
  K. N., Int. J. Mod. Phys. A18 (2003) 4053

## Slide 3: What is Hyper-Kamiokande ?
～1 Mton water Cherenkov detector at Kamioka

## Slide 4: Why this design has been chosen ?
Water depth < 50 m
  (If the present 20-inch PMT or similar one will be used.)
Linear dimensions for light path < 100 m
Optimization of MFID/MTOTAL
Rock stability
  Avoid sharp edges. Spherical shape is the best.
Our solution: Tunnel-shaped cavity
Single Cavity or Twin Cavities?
  Single Cavity
    MFID/MTOTAL is better
    Cost is lower
    Larger area of stable rock mass needed.
  Twin Cavities
    Two detectors are independent. One detector is alive when the other is calibrated or maintained.
    Both cavities should be excavated at the same time. But staging scenario is possible for the later phase of the detector construction.
Our solution: Twin cavities

## Slide 5: Size of the detector
Fiducial volume: 39mφ×45m ×5 sections ×2 = 0.54 Mton
Total Inner detector volume: 43mφ×49m ×5 sections ×2 = 0.72 Mton
Total detector volume: 1 Mton
Total number of PMTs: 200,000 (if 2/m2)
Fiducial / Total

## Slide 6: Comparison of 3 Generations of Kamioka Nucleon Decay Experiments
Kamiokande Super-Kamiokande Hyper-Kamiokande
Mass 3,000 t 50,000 t 1,000,000 t
(+1,500 t)
Photosensitive 20 % 40 % (SK-I and -III) ?
Coverage 20 % (SK-II)
Observation 1983 1996 ?
Started
Cost (Oku-Yen)* 5 100 500?**
* 1 Oku-Yen  1M$
** Target cost; No realistic estimate yet

## Slide 7: Construction Time Line
2008 | 09 | 20 10 | 11 | 12 | 13 | 14 | 20 15 | 16 | 17 | 18 | 19 | 2020 | 21 | 22 | 23
T2K-I
HK construction
HK and T2K-II experiment

## Slide 8: What can be done with Hyper-K ?
T2K long baseline neutrino oscillation experiment:
  2nd phase, CP violation
  If the 13 measurement in the 1st phase gives only an upper limit, the 2nd phase will enhance the reach
Proton decay
  e+π0
  νK+
  and other modes
Neutrino oscillation measurements with atmospheric neutrinos: 13, sgn(m2), sub-dominant osc., CP phase
Measurements of low-energy neutrinos
  Supernova neutrino (～x105 neutrinos for
  a SN at the center of the galaxy)
  Relic supernova neutrinos
  Solar neutrino measurements
    Possible at the Hyper-K site (600-700 m
    overburden) ? Under study.
  Reach: p(e+0)/B  1035 yr
  p(K+)/B  1034 yr
Shiozawa
Kobayashi
Kajita
Nakahata’s study for
Mton water Cherenkov
detectors in gereral
 beam of ~1GeV
Kamioka
J-PARC
→ x disappearance
→ e appearance
NC measurement
~Mt “Hyper Kamiokande”
0.75 MW 50 GeV PS
4MW 50 GeV PS
CPV
proton decay
1st Phase
2nd Phase
Super-K: 50 kton
Water Cherenkov

## Slide 9: Status of Hyper-K Planning and R&D
Site studies: Tochibora mine has been selected. Overburden 600 – 700 m
Cavity design and excavation studies:Twin cavities preferred; FEA in progress; Geological survey and boring core studies made with existing data; in situ measurement of initial rock stress yet to be done; direct exploration boring and geo-survey tunneling at the candidate site needed, etc.
Water tank and PMT support: Conceptual design started, but progress is slow.
Spherical HPD: 5-inch prototype tested, 13-inch prototype test in progress.
Realistic cost estimation: Yet to be done
Study trade-off between physics capabilities and photocoverage (i.e., cost): Partly done for p→e+0, but many more studies needed.
Nakagawa
Aihara
Shiozawa
Kamioka Mine
Geological Map
MOZUMI
Mine
TOCHIBORA
Mine