## Slide 1: Revisiting the optimum PMT size for water-Cherenkov megaton detectors
Esso Flyckt, Christophe Fontaine, Pascal Lavoute and Carole Marmonier
Photonis, Brive, France
NNN05 workshop
Aussois 2005-04-08

## Slide 2: Overview
PHOTONIS
Physics is challenging
Traditional PMTs
Optimal size <=> cost
Capacity & investments
Sub-conclusions
Discussion
R&D prospects

## Slide 3: Brive
RODEN
BRIVE
1937
PHILIPS BRIVE
1963
HYPERELEC
1986
RTC Compelec
1990
PHILIPS
COMPONENTS
1992
PHILIPS
PHOTONICS
1998
PHOTONIS
2005
PHOTONIS-DEP

## Slide 4: PHOTONIS
Photomultipliers
Image intensifiers
Streak tubes
Microchannel plates
Single-channel electron multipliers
Neutron detectors

## Slide 5: PMTs
Nuclear medicine (~80%)
    gamma cameras
    PET scanners
Analytics/industrial (~10%)
Physics (~10%)

## Slide 6: H.E.S.S. in Namibia (very-low after-pulse PMT)

## Slide 7: Veritas in Arizona

## Slide 8: Auger in Argentina

## Slide 9: Traditional PMTs
Hemispherical
5“, 8“, 9“,
10.6“, 12“, 15“

## Slide 10: Very many PMTs Example: UNO >50,000x 20“
PMT size <=> cost
Embedded inside water volume
Sensitivity
Timing
SE pulse-height resolution
Granularity

## Slide 11: PMT size <=> cost
Diameter 20“ <=> (20“)17“ <=> 12“
projected area 1660 1450 615 cm²
QE(typ) 20 20 24 %
CE 60 60 70 %
Cost 2500 2500 800 €
Cost/cm² per useful PEU= cost/(cm²xQExCE)
12.6 14.4 7.7 €/PEU/cm²

## Slide 12: Timing-Weight
Size | 20“ | 17“ | 12“
Rise time (ns) Jitter (ns) | 10 5.5 | 6 3.4 | 5 2.4
Weight (kg) 8 8 2.2

## Slide 13: Single-electron resolution
Need good P/V for exact gain calibration:
  20“ difficult? (P/V = 1.1 - 1.7:1)
  17“ P/V = 1.5 - 2.5:1 (reality better)
  12“ P/V = 1.5 - 2.3:1 (reality better)

## Slide 14: Quantities and total cost
20“ 50,000 x € 2500 = € 125M
17“ 57,200 x € 2500 = € 143M
12“ 135,000 x € 800 = € 108M

## Slide 15: New pump capacity needed?
Delivery over 6 years
300 working days/year
  20“ tube
    50,000/6/300 => 28 good tubes x yield 0.7 = 40 starts/day
    (1 start/pump/day) => 40 pumps ( € 7M or so)
  12“ tube
    135,000/6/300 => 75 good tubes x yield 0.7 = 110 starts/day.
    A multi-array computerised pump at Photonis handles 20 starts/day
    => 6 pumps ( € 2M or so)

## Slide 16: + Sub-conclusions
12“ seems much better than 20“/17“
cost per useful photoelectron & total PMT cost
timing
single-electron resolution (17“ equal)
granularity
weight and handling
implosion risk
investments and start-up

## Slide 17: - Sub-conclusions
cost of more cables and electronics
12“ tubes may also need a shield at 60 m depth (or thicker glass?)

## Slide 18: Discussion
The 12“ tube is a cost-optimum for Photonis pumping systems - maybe other cost-optima in 8“ - 15“ for other suppliers?
Can be made by at least 4 suppliers - without major R&D!
Photonis is willing, able and prepared up to 15“
However, non-industry investments needed!

## Slide 19: Optimise! Cost/cm² per useful PEU= cost/(cm²xQExCE)

## Slide 20: Invest in QE now!
Instead of investing € 7M (or so) for 20“ it is better to
  invest € 2M (or so) for 12“ and
  another € 0.5M in getting the QE up to > 30 %
Photonis has such a QE programme
Characterisation with French institutes

## Slide 21: „Smart“ PMTs so far
„smart“ => PHR => elimination of single PE noise (for DUMANDs)
Patented by Philips (Photonis)
Copied (faster mushrom shape) by INR, Moscow, into the „QUASAR“
Philips (spherical)

## Slide 22
anode target was YSO single-crystal at +25-30 kV =>
photocathode at ground potential!
partly sensitive from the back

## Slide 23: Pulse-height resolution
S/N 8 & 10 deployed in Lake Baikal

## Slide 24: Status „smart“ PMTs
Philips/Photonis made ~ 30; invested 1M €!
200 QUASARs operating for many years in Lake Baikal => proof of concept as to life time!
No ongoing production!
Could be made (and improved) again!

## Slide 25: Possible „smart“ PMTs
Reproduce and improve former tubes
Redesign (target)
  Better scintillator (LSO, ZnO:Ga, ...)
  Si diode/Si diode array
  APD/APD array
  Multianode multiplier
  Quadrant PMT (inside/outside)
  ??

## Slide 26: On-going R&D
„smart“ 8 => 12“ tubes with:
  electron-bombarded scintillator in a preamplifier tube, read-out by a small, fast PMT
  electron-bombarded Si diode as the anode
Both will resolve 1, 2, 3, several photoelectrons but - need to stand > 15 - 20 kV
Is such „smartness“ worth a factor 2-3 in cost?

## Slide 27: Photonis has all the technical capability needed! R&D cooperation: detailed & intensive talks are going on with the MEMPHYS collaboration to define a balanced programme Workshop planned in the spring

## Slide 28: Questions?