## Slide 1: Online and offline data handling for large detectors (designed for non-accelerator experiments)
Yoshinari Hayato (ICRR)
Introduction
Difficulty ( Water Cherenkov detector )
Data transfer via Ethernet
High Availability
Data format for the online system
In designing the data handling system
Use of the database
Summary

## Slide 2
Introduction
Requirements for the online/DAQ system are
(slightly) different from the “accelerator” based experiment.
Rare events ( nucleon decay, super nova etc.)
can happen “at any time”.
Natural neutrino beam is always there.
Order of the events is also important.
Triggered by the detector (system) itself.
Dead-time needs be minimized
Dead-time should be recorded.
Condition of the detector is necessary to be recorded.
Large neutrino and nucleon decay detector
Keep the detector running “all the time” without dead-time.
1) Dead-time (down time) due to the equipment trouble or maintenance
2) Dead-time due to the limitation of the DAQ/online system
Electron generated by decay of 
might be misidentified as the product of e scattering.
Low energy events might be generated by spallation products

## Slide 3
2nd event
Difficulty
(Water Cherenkov detector and relatively extreme?? case)
Example of a very low energy event:
2.2 MeV  (from neutron capture) generates only ~6 PMT hits in SK.
If one want to detect very low energy events,
trigger rate gets extremely high.
(This depends on the radio activity in the water
and isolation from the surrounding rock.)



1st event
t
Due to a trigger generated by a small activity,
“real high energy  event” can be split into two.
Notes: t

## Slide 4
Simple solution
Record all the hits from PMTs including dark noise.
Then, apply the “software” trigger and define an event.
Realistic??
Assume 10kHz dark rate and data size of 6bytes/PMT hit
~840MB/sec for a detector with 14k PMTs.
(Typical dark rate of PMT in SK is 3~5kHz.)
Front-end board
Front-end board
Front-end board
Front-end board
readout system
readout system
Hits sorter + Merger
Hits sorter + Merger
Intelligent trigger system
Offline system
(analysis & storage)
Possible design ( Schematic diagram of data flow part )
Ethernet
or dedicated data bus
Ethernet
used to be “event-builder”
Sort PMT hits
in the order of timing.

## Slide 5
Data transfer via Ethernet
Network is quite reliable but not perfect, as always.
Even TCP/IP might be a cause of problem.
Device driver or network equipment might be broken or buggy.
Some defects in equipment or software creates corrupted data.
Careful design of the network is very important.
Traffic analysis
including typical packet (data block) size estimation
Monitoring point (where and how to tap etc…)
Network performance heavily depends
on the size of each data packet
and the design of the network topology.
The characteristic of the data flow of online/DAQ system
is different from the usual client-server system.
Usually, the server sends large amount of data
based on the request from a client.
In the DAQ system, server “collects” data.
The network components are ( sometimes ) designed
to maximize their performance for the “usual” client-server model.

## Slide 6
Stand-by
Readout #2
High availability (HA) system
In the online/DAQ system
one of the computer will be down at any moment.
To reduce downtime of the detector,
concept of the HA system seems to be useful and attractive.
Always monitor the status of the system (computers).
Once one of the computer seems to have problem,
the stand-by machine starts working.
(Used for web, database and disk servers.)
Usually, complete replica of the server is prepared.
For the online/DAQ system, it is quite symmetric and thus,
only a few backups for each system will be sufficient.
Readout #2
Readout #1
Status monitor
Merger
Stopped….
Example
Dedicated line for the status monitoring
Data path

## Slide 7
Simple format and embedded “easy to identify” tags are always very useful.
Data format used in the online system
Could be different from the one used in the offline system.
Also, it is helpful
to keep the “original” form of the (corrupted) data
in identifying the cause of a trouble in the offline format.
You may need to capture and analyze data on the network
to investigate the problem.
It is not easy to keep up with the updates of the offline software.
Once you start the experiment,
people want to take data as much as possible.
But simple update of the library
may cause “unexpected” troubles…
Preparing a data format converter
is easier and safer in various reasons, still.

## Slide 8
Front-end board
Monitoring the data quality
and the quick detection of errors
are important issues
Error detection - Possible check points:
1) Electronics (front-end board)
2) Readout system
3) Hits sorter + Merger
4) Intelligent trigger system
5) Data quality monitor
Traceability
Sorter + Merger
Intelligent trigger system
Readout system
Offline system
In designing the data handling system
At each checkpoint, characteristics of accumulated data are different.
Monitor data quality at each point will be effective.
Necessary for the troubleshooting.
You may want to analyze data
with minor troubles.
To understand the situation,
it is necessary to keep “erroneous” data.

## Slide 9
In designing the data handling system
There might be no PMT hits in a board
for certain period of time.
Front-end board
Hit sorter + Merger
Intelligent trigger system
Readout system
Offline system
1st check point
Front-end electronics board
Recent FPGA can provide smart hardware level error detection.
In preparing the error detection code,
don’t forget to keep both the error information
and “erroneous data” themselves.
One requirement for the electronics
(in the continuous data taking mode)
The front-end board should be designed
to generate periodic “heart beat” signal.
It is difficult to identify
whether the board without PMT hits
was alive or not in the later check points.

## Slide 10
Also, this computer will allow you
to test the system in the “standalone mode”.
And you can run the remaining part of the detector.
Readout system can be consists of
hardware modules only.
It will be robust in one sense.
And thus, it is possible to perform
detailed consistency check of the data here.
Front-end board
Sorter + Merger
Intelligent trigger system
Readout system
Offline system
In designing the data handling system
2nd check point
Readout system
Because each readout system does not handle
not so many PMT hits.
(Too much data makes you trouble in finding errors.)
But I (personally) think it is better
to have a computer in the system
at least for the error detection.

## Slide 11
In applying the intelligent-trigger,
it is very important to keep
the revisions of the calibration constants
and software used to select (define) an event.
Same kind of information should be kept
in the offline analysis as always.
For example, missing block need to be “corrected” in the calorimeters.
Front-end board
Sorter + Merger
Readout system
Next check points
Hit sorter + Merger
Intelligent trigger system
Offline analysis
Here, it is possible to use
all the hits from entire detector.
Intelligent trigger system
In designing the data handling system
Offline system
Also, the relation between the raw data ( raw hits )
and the reconstructed results should be kept.
Slow monitor information (low voltage/high voltage, temperature etc.)
are also very important.

## Slide 12
As a (raw) data storage system,
there will be a problem in distributing data.
Of course, database is very useful in various cases.
Examples:
Keep tracks of calibration constants.
In the accelerator based long baseline experiments,
it will be very convenient to keep the beam timing
and the beam properties in the database.
Most of the time, simple(?) data base system is enough.
ROOT, Berkeley DB etc…
Use of the database
(Personal opinion.)
Data replication is possible but not so simple.
Supporting various data access method (direct file I/O & DB I/F)
might cause problem.
But it is not necessary to use famous Relational Database.
(Oracle, PostgreSQL, mySQL etc.)

## Slide 13
Summary
Even from the water Cherenkov type detector,
total amount of data could be a few GB/sec.
It is not impossible to handle this data with recent technology
but the system should be designed carefully.
The loss of the data is really critical in the analysis.
Always keep in mind
how to detect and investigate troubles.
To reduce the down time,
the concept of HA system will be useful.
It is necessary to recognize the characteristic of the data flow
in the online/DAQ system is different
from the usual network traffic.
The design of the network system is important.
Size of the packets might be a problem.