## Slide 1: Pion Yields from a Tantalum Rod Target using MARS15

Comparisons across proton driver energies and other parameters

## Slide 2: Contents
Problem and parameters
Variation of proton energy
  Total pion yield
  Simple cuts
  Probability map “cuts” from tracking
Investigation of the hole
Variation of rod radius
Notes on effect of rod length and tilt angle

## Slide 3: Basic Setup
Pions counted at rod surface
B-field ignored within rod (for now)
Proton beam assumed parallel
  Circular parabolic distribution, rod radius
Rod is not tilted
20cm
1cm
Solid Tantalum
Protons
Pions

## Slide 4: Possible Proton Energies
Proton Driver | GeV
SPL | 2.2
 | 3
 | 4
RAL green-field study | 5
RAL/ISIS 5MW | 6
RAL/ISIS 1MW, FNAL linac | 8
 | 10
RAL/ISR | 15
 | 20
RAL/PS, JPARC initial | 30
 | 40
JPARC final | 50
 | 75
 | 100
FNAL injector/NuMI | 120

## Slide 5: Total Yield of + and −
Normalised to unit beam power (p.GeV)
NB: Logarithmic scale!
66% more + at 30GeV than 2.2GeV
57% more − at 30GeV than 2.2GeV

## Slide 6: Energy Deposition in Rod (heat)
Scaled for 5MW total beam power; the rest is kinetic energy of secondaries

## Slide 7: Total Yield of + and −
Normalised to unit rod heating (p.GeV = 1.6×10-10 J)
From a purely target point of view, ‘optimum’ moves to 10-15GeV

## Slide 8: Angular Distribution
2.2GeV
6GeV
15GeV
120GeV
Backwards
+ 18%
− 33%
8%
12%
8%
11%
7%
10%

## Slide 9: Angular Distribution
What causes the strange kink in the graph between 3GeV and 5GeV?

## Slide 10: Some Artifacts?
MARS15 uses two hadron production models:
  The “Cascade-Exciton Model” CEM2003 for E<5GeV
  “Inclusive” hadron production for E>3GeV
Nikolai Mokhov says:
A mix-and-match algorithm is used between 3 and 5 GeV to provide a continuity between the two domains. The high-energy model is used at 5 GeV and above. Certainly, characteristics of interactions are somewhat different in the two models at the same energy.
Your results look quite reasonable, although there is still something to improve in the LANL's low-energy model, especially for pion production. The work is in progress on that. A LAQGSM option coming soon, will give you an alternative possibility to study this intermediate energy region in a different somewhat more consistent way.

## Slide 11: Possible Remedies
Ideally, we would want HARP data to fill in this “gap” between the two models
K. Walaron at RAL is also working on benchmarking these calculations against a GEANT4-based simulation
Activating LAQGSM is another option
We shall treat the results as ‘roughly correct’ for now, though the kink may not be as sharp as MARS shows

## Slide 12: Summary 1
So far, it appears that a 10-30GeV proton beam:
  Produces ~60% more pions per p.GeV
  …in a more focussed angular distribution
  …with ~40% less rod heating
…than the low-energy option
BUT: the useful yield is crucially dependent on the capture system
With certain provisos on the accuracy of MARS’s pion model over the transition region

## Slide 13: Simple Cuts
It turns out geometric angle is a badly-normalised measure of beam divergence
Transverse momentum and the magnetic field dictate the Larmor radius in the solenoidal decay channel:

## Slide 14: Simple Cuts
Acceptance of the decay channel in (pL,pT)-space should look roughly like this:
pL
pT
Larmor radius = ½ aperture limit
Angular limit (eliminate backwards/sideways pions)
Pions in this region transmitted
max
pTmax

## Slide 15: Simple Cuts
So, does it?
Pions from one of the MARS datasets were tracked through an example decay channel and plotted by (pL,pT)
  Coloured green if they got the end
  Red otherwise
This is not entirely deterministic due to pion  muon decays and finite source

## Slide 16: Simple Cuts
So, does it?

## Slide 17: Simple Cuts
So, does it? Roughly.

## Slide 18: Simple Cuts
So, does it? Roughly.
If we choose:
  max = 45°
  pTmax = 250 MeV/c
Now we can re-draw the pion yield graphs for this subset of the pions

## Slide 19: Cut Yield of + and −
Normalised to unit beam power (p.GeV)
High energy yield now appears a factor of 2 over low energy, but how much of that kink is real?

## Slide 20: Cut Yield of + and −
Normalised to unit rod heating
This cut seems to have moved this optimum down slightly, to 8-10GeV

## Slide 21: Tracking through Two Designs
Possible non-cooling front end
  Uses bunch compression chicane after decay channel
  Then an 88MHz muon linac to 400±100MeV
RF phase-rotation system
  Continues the linear solenoid channel
  31.4MHz cavities reduce the energy spread
  Goal is 180±23MeV for cooling ring injection

## Slide 22: Fate Plot for Chicane/Linac
Magenta | Went backwards
Red | Hit rod again
Orange | Hit inside first solenoid
Yellow/Green | Lost in decay channel
Cyan | Lost in chicane
Blue | Lost in linac
Grey | Wrong energy
White | Transmitted OK
(Pion distribution used here is from a 2.2GeV proton beam)

## Slide 23: Fate Plot for Phase Rotation
Magenta | Went backwards
Red | Hit rod again
Orange | Hit inside first solenoid
Yellow/Green | Lost in decay channel
Blue | Lost in phase rotator
Grey | Wrong energy
White | Transmitted OK

## Slide 24: Probability Grids
Can bin the plots into 30MeV/c squares and work out the transmission probability within each
Chicane/Linac
Phase Rotation

## Slide 25: Probability Grids
Can bin the plots into 30MeV/c squares and work out the transmission probability within each
These can then be used to estimate the transmission quickly from MARS output datasets at various proton energies

## Slide 26: Chicane/Linac Transmission
Energy dependency is much flatter now we are selecting pions by energy range
Normalised to unit beam power (p.GeV)

## Slide 27: Chicane/Linac Transmission
Normalised to unit rod heating
6-10GeV now looks good enough if we are limited by target heating

## Slide 28: Phase Rotator Transmission
Normalised to unit beam power (p.GeV)

## Slide 29: Phase Rotator Transmission
Normalised to unit rod heating

## Slide 30: Summary 2
While 30GeV may be excellent in terms of raw pion yields, the pions produced are increasingly lost due to:
  Large transverse momenta (above 10-20GeV)
  A high energy spread, outside the acceptance of bunching systems (above 6-10GeV)
This work suggests the optimal energy is around 6-10GeV, providing a 50% yield improvement over 2.2GeV
With certain provisos on the accuracy of MARS’s pion model over the transition region

## Slide 31: Rod with a Hole
Idea: hole still leaves 1-(rh/r)2 of the rod available for pion production but could decrease the path length for reabsorption
Rod cross-section
r
rh

## Slide 32: Rod with a Hole
Idea: hole still leaves 1-(rh/r)2 of the rod available for pion production but could decrease the path length for reabsorption
Used a uniform beam instead of the parabolic distribution, so the per-area efficiency could be calculated easily
r = 1cm
rh = 2mm, 4mm, 6mm, 8mm

## Slide 33: Yield Decreases with Hole
30 GeV
2.2 GeV

## Slide 34: Yield per Rod Area with Hole
30 GeV
2.2 GeV
This actually decreases at the largest hole size!

## Slide 35: Rod with a Hole Summary
Clearly boring a hole is not helping, but:
The relatively flat area-efficiencies suggest reabsorption is not a major factor
  So what if we increase rod radius?
The efficiency decrease for a hollow rod suggests that for thin (<2mm) target cross-sectional shapes, multiple scattering of protons in the tantalum is noticeable

## Slide 36: Variation of Rod Radius
We will change the incoming beam size with the rod size and observe the yields

## Slide 37: Variation of Rod Radius
We will change the incoming beam size with the rod size and observe the yields
This is not physical for the smallest rods as a beta focus could not be maintained
Emittance x | Focus radius | Divergence | Focus length
25 mm.mrad extracted from proton machine | 10mm | 2.5 mrad | 4m
 | 5mm | 5 mrad | 1m
 | 2.5mm | 10 mrad | 25cm
 | 2mm | 12.5 mrad | 16cm

## Slide 38: Variation of Rod Radius
We will change the incoming beam size with the rod size and observe the yields
For larger rods, the increase in transverse emittance may be a problem downstream
Effective beam-size adds in quadrature to the Larmor radius:

## Slide 39: Total Yield with Rod Radius

## Slide 40: Cut Yield with Rod Radius
Rod heating per unit volume and hence shock amplitude decreases as 1/r2 !
Multiple scattering decreases yield at r = 5mm and below
Fall-off due to reabsorption is fairly shallow with radius

## Slide 41: Note on Rod Tilt
All tracking optimisations so far have set the rod tilt to zero
The only time a non-zero tilt appeared to give better yields was when measuring immediately after the first solenoid
Theory: tilting the rod gains a few pions at the expense of an increased horizontal emittance (equivalent to a larger rod)

## Slide 42: Note on Rod Length
Doubling the rod length would:
  Double the heat to dissipate
  Also double the pions emitted per proton
  Increase the longitudinal emittance
The pions already have a timespread of RMS 1ns coming from the proton bunch
The extra length of rod would add to this the length divided by c

## Slide 43: Conclusion
Current results indicate 6-10GeV is an optimal proton driver energy for current front-ends
  If we can accept larger energy spreads, can go to a higher energy and get more pions
A larger rod radius is a shallow tradeoff in pion yield but would make solid targets much easier
Tilting the rod could be a red herring
  Especially if reabsorption is not as bad as we think
So making the rod coaxial and longer is possible

## Slide 44: Future Work
Resimulating with the LAQGSM added
Benchmarking of MARS15 results against a GEANT4-based system (K. Walaron)
Tracking optimisation of front-ends based on higher proton energies (sensitivity?)
Investigating scenarios with longer rods
  J. Back (Warwick) also available to look at radioprotection issues and adding B-fields using MARS