## Slide 1: LAL Horn R&D
J.E Campagne, A. Caze (Ph. D),
CNGS Horn: G. Macé, S. Wallon
New persons: J. Bonis, M. Omesh,…
Other IN2P3 members: J. Dumarchez (LPNHE), D. Autiero (IPNL), S. Katsanevas(IN2P3-adm)

## Slide 2: Our plans
Start with the CERN Horn design and appreciate what are the critical points.
Secondary particles focalisation & energy deposit:
  A.Cazes has started to introduce the geometry and material content as close as possible to the real drawing in a GEANT3 based simulation. Thanks to S. Gilardoni who provides him outgoing Hg-TARGET particles 4-vectors, he has some very preliminary results to be compared with already existing results (in private).
  Then, improvement/systematic (hadronic interactions…)
  Q: deposit energy 15kW/4MW proton beam? Optimisation of the conductor profile, materials?
Electrical power supply:
  M. Omesh has started to study the design for the « final » power supply (300kA/50Hz,100s)
  Q: dedicated feasability tests?

## Slide 3: Our plans (continued)
Mechanical Simulation: considered to be conducted first to determine the minimal thickness of the Inner Conductor.
  Q: cyclic constraints on the IC? Lifetime of the Horn?
Thermal Simulation: considered as the second step, to determine the Inner Conductor cooling system (T < 100°C).
  We need to measure the convection coefficients or thermal transmissibility (to alleviate factor 2 uncertainty in the literature, 2000-4000w/m2/K). Need a dedicated setup (next slide) which may be also useful to test different kinds of cooling systems.
  Q: TARGET cooling enough or add kW to the existing contributions? Separate or join TARGET and hottest part of the Horn cooling systems? Do we need a double skin?

## Slide 4: Longitudinal section
Glass insulator disc
Outer skin
Inner skin
Water outlet
Electrical connections
to the strip-lines
Water inlets (circuit 2)
Water inlets
(circuit 2)

## Slide 5
Aluminum alloy cylinder
80 mm ext. diameter
300 mm length (min.)
Water inlets
Sprinkler
Water curtain
Tank
IR heater
(or heater rings on
cylinder inner surface)
Heat load ~ 25 kW
About 10 temp. probes
on outer surface
Or other water jets
configuration

## Slide 6: Our plans (continued)
Mechanical properties modifications under high neutron flux:
  A bibliographical research has been conducted (see MEMO as NuFact note soon) thanks to a contact with French CEA experts of the SEMI laboratory.
  Discussion with TARGET group to understand the neutron flux spectrum. Q: there is no thermal component even indirect by activation of the environment?
  Envisaged: contact with Belgium colleagues of the CEA to establish collaboration: measurements of resistance fatigue limit of irradiated 6061T6 Alu (nuclear reactor) up to 109 cycles. (cost estimate of similar request ~300 k€). Q: Is the Rf ~ Rm/3 still valid for irradiated materials with He cavities appearing for > 6 1022 nfast/cm2? Pb of Reactor irradiation: 2 1023nTh/cm2 so Si production & precipitation with Mg effect is preponderant.
  In parallel do the same test for non-irradiated material (notched and unnotched) by ultrasonic method (at CNAM Paris: ~ 4 k€). Q: what is the maximum stress applicable after 109 cycles?

## Slide 7: Time
We should be able to dispose by June 03:
  Simulation results (A.C + J.E)
  Mechanical/Thermal theoretical summary notes (S.W)
  The water cooling setup test (S.W + J.B)
  May be a first cost estimate of test with irradiated materials.
Next goal: a new Test facility with a new Horn, new power supply, new cooling system… (2005?)
The question for us is the level of engagement (money) that will be offered by IN2P3. For the moment LAL engagement relies on internal resources which cannot be enough for sure!!!???