## Slide 1: Un grand laboratoire au Fréjus pour MEMPHYS ?
Coût estimé 1 cavité stabilisée ≈ 80 M€
Equipé de 80,000 PMTs 12’’ ≈ 80 M€
Résultat d’une étude préliminaire par la Société SETEC (constructeur du tunnel)
Tunnel de Sécurité:
mars 2006 8.20m Comité de Sécurité Franco-Italien
21 avril 2006 8.00m “utiles” par la Commission Inter-Gouvernementale Franco-Italienne
Le LSM dans sa forme actuelle
65m
SK
65m
3 puits = 440kT fid.,
1 puits = 4xSK

## Slide 2: Les détecteurs Čerenkov à Eau dans le monde
 | UNO (USA) | HK (Japon) | MEMPHYS (EU)
Laboratoire |  |  | 
lieu | Henderson/Homestake | Tochibora | Fréjus
prof. Mwe | 4500/4800 | 1500 | 4800
LBL(km) | 1480÷2760/1280÷2530 | 290 | 130
Dimsensions du détecteurs |  |  | 
type | 3 cubes | 2 tunnels de 5 compartiments | 3 à 5 puits
dimension | 60x60x60m3 | 43m x L:50m | 65m x L:65m
M fid. Kt | 440 | 550 | 440 à 730
Photodetecteurs |  |  | 
type | 20’’ PMT | 20’’ H(A)PD | 12’’ PMT
# | 38000 (milieu) 2 x 9500 (coté) | 20,000 par compartiment | 81,000 par puit
Couverture | 40%/10% (milieu/coté) | 40% | 30%
Coût estimé… |  |  | 
 | 500M$ | 500 Oku ¥ | 161M€ x #puits +100M€ infra.
50% excavation + 50% Photodetection

## Slide 3: R&D Photodetecteurs
1st peak
2nd peak
0 p.e.
30,000 electrons
1 p.e.
HPD
H. Aihara @ NNN05
20kV !
Hamamatsu R&D
Needs low noise electronics
Diameter 20“ <=> 12“
projected area 1660 615 cm²
QE(typ) 20 24 %
CE 60 70 %
Cost 2500 800 €
Cost/p.e/cm 13 8 €
→ 20’’
PMT Photonis@NNN05

## Slide 4: R&D Electronique
Integrated readout : “digital PM (bits out)”
  Charge measurement (12bits)
  Time measurement (1ns)
  Single photoelectron sensitivity
High counting rate capability (target 100 MHz)
Large area pixellised PM :
  16 low cost PMs
  Centralized ASIC for DAQ
  Variable gain to have only one HV
Multichannel readout
  Gain adjustment
  Subsequent versions of OPERA_ROC ASICs
Network
  Wireless?
IPNO-LAL-LAPP

## Slide 5: French funding agency (ANR ≠ CNRS/IN2P3 and CEA)
Demand for a Joint R&D :
  LAL-IPNO-LAPP
  Photonis Co.
  3years, 400k€, 1FTE physicist, 5FTE Engineers
LAL: electonics: 100k€ + 1 post-doc
IPNO: photodetector tests + mechanics: 18Ok€
LAPP: Data network: 53k€
Photonis: PMTs provider: 64k€
Expected answer in July 06

## Slide 6
Year 2005 2010 2015 2020
Safety tunnel
Excavation
Lab cavity
Excavation
P.S
Study
detector
PM R&D
PMT production
Det.preparation
Installation
Outside lab.
P-decay, SN
Construction
Superbeam
Beta beam
Construction
decision for cavity digging
decision for CERN SPL construction
decision for EURISOL site at CERN
Guideline for a megaton scale Water Cherenkov
When?

## Slide 7: Commentaire à Stavros