## Slide 1: LAL Horn R&D
Physicists: J.E Campagne, A. Caze (Ph. D),
Engineers: G. Macé, S. Wallon & J. Bonis, M. Omesh,…
Previous experience: the CNGS Horn/Reflector
Other IN2P3 members:
J. Dumarchez (LPNHE), D. Autiero (IPNL), S.Katsanevas(IN2P3-adm)

## Slide 2: Competence examples for CNGS
T=24°C
T=33°C
Thermal study
Cyclical thermal stress
stress
Dynamic study
Installation/Replacement
Cyclical mechanical
stress
Model for FEM analysis

## Slide 3: Our plans for the near future R&D
Secondary particles collection simulation
  optimise the collection property and the deposit energy for 4MW proton beam
Electrical power supply studies:
  study with CERN the design for the « final » power supply (300kA/50Hz,100s): contact with firm form price estimation
Mechanical Simulation: (material: Alu 6082 qualified for CNGS):
  determine first the minimal thickness of the Inner Conductor (6+2mm -> 2mm?) to decrease the power dissipation due to the particles themselves (Cyclical mechanical stresses calculation)
Thermal Simulation:
  determine the Inner Conductor cooling system (T < 80°C).
  Cyclical thermal stresses studies
  But we need to measure the convection coefficients (2000-4000w/m2/K for water) in different configurations.
  Main uncertainty: heat load from the Target itself (new)?
Start with the CERN Horn (see S. Gilardoni talk, NuFact 129 note)
and try to simplify the design to understand the real needs.

## Slide 4
Mechanical properties modifications under high neutron flux:
  A bibliographical research has been conducted (see MEMO as NuFact 130) thanks to a contact with French CEA experts of the SEMI laboratory.
  Question: measurements of fatigue strength of irradiated 6000-like Alu up to 109 cycles. Is the D~ uts/3 still valid for irradiated materials with He cavities appearing for > 6 1022 nfast/cm2? Pb of Reactor irradiation: in general 10 times more thermal neutrons with respect to fast neutrons, and for 2 1023nTh/cm2 or so Si production & precipitation with Mg effect is preponderant.
  In parallel do the same test for non-irradiated material (notched and unnotched) by ultrasonic method (at CNAM Paris). Determine the maximum stress applicable after 109 cycles? (note 14MPa static stress on the waist of 3mm thick)
Start this year as soon as possible…