## Slide 1: Parameters of 2nd SPL feasibility study
A.M.Lombardi
(reporting for the working group)

## Slide 2: Contents
what has changed with respect to CDR1 [=conceptual design report]
frequency/ length /RF power/reliability and cost
energy and synergy
contributors to CDR2
planning and conclusions

## Slide 3: CDR1 baseline
SPL-CDR1 design was based on re-using the de-commissioned LEP RF system (50 Klystrons at 352 MHz) with new SC cavities (beta < 1.0, Nb sputtered on Cu).
frequency fixed to 352 MHz,
final energy fixed to 2.2 GeV
Design tailored to the Neutrino Factory

## Slide 4: SPL block diagram (CDR 1)
SPL1 : 0 to 2.2 GeV in 650 meters

## Slide 5: SPL beam characteristics (CDR 1)
Ion species | H- | 
Kinetic energy | 2.2 | GeV
Mean current during the pulse | 13 | mA
Duty cycle | 14 | %
Mean beam power | 4 | MW
Pulse repetition rate | 50 | Hz
Pulse duration | 2.8 | ms
Bunch frequency (minimum distance between bunches) | 352.2 | MHz
Duty cycle during the pulse (nb. of bunches/nb. of buckets) | 62 (5/8) | %
Number of protons per bunch | 4.02 108 | 
Normalized rms transverse emittances | 0.4 |  mm mrad
Longitudinal rms emittance | 0.3 |  deg MeV
Bunch length (at accumulator input) | 0.5 | ns
Energy spread (at accumulator input) | 0.5 | MeV
Energy jitter during the beam pulse | < ± 0.2 | MeV
Energy jitter between pulses | < ± 2 | MeV

## Slide 6: push for change
very good results on beta<1 700MHz bulk niobium SC cavities
global view on the costing of 352 vs. 700 MHz
2.2 GeV is a perfectly suited energy for a neutrino factory but not for a super beam
A direct superbeam from a 2.2 GeV SPL does not appear to be the most attractive option for a future CERN neutrino experiment as it does not produce a significant advance on T2K. from SPSC-Villars04 recommendation

## Slide 7: gradients at 700 MHz
Last test performed in CryHoLab (July 04):
5-cells 700 MHz ß=0.65 Nb cavity A5-01
from CEA/Saclay and IPN-Orsay
from Stephane Chel, HIPPI04, Frankfurt, sep04

## Slide 8: gradients at 700 MHz
  Magnetic field limitation is a basic physics constraint, for Nb the hard limit is of the Order of 200 mT.
  Electric field limitation is set by the technological processes: material, treatments, handling and cleanness. The cavity shape has shown playing a crucial role while frequency has very little, if any, influence.

## Slide 9: surface field doesn’t depend on frequency or beta
Paolo Pierini, INFN MILANO, DRAFT

## Slide 10: the ratio of surface electric/magnetic field to accelerating field increases rapidly at decreasing beta
Paolo Pierini, INFN MILANO, DRAFT

## Slide 11: the reduction of the beta of the cavity implies smaller inductive and capacitive volumes, thus leading to higher surface fields.
Paolo Pierini, INFN MILANO, DRAFT

## Slide 12: RF sources at 700 MHz
1 MW foreseen for 2007 in Cryolab (saclay)
4MW available from Thales (priced already at 1 MEuros)
there is a big jump (price, complexity) between a pulsed source (up tp 2 msec 50Hz, i.e. 10% duty cycle) and a CW one therefore power upgrades above 10 MW can be achieved only by increasing the final energy or the current

## Slide 13: CDR2 baseline
3 families of cavity : beta =0.5,0.85,1.0
gradients : 15, 18, 30 MV/m
5, 6 and 7 cells per cavity

## Slide 14: CDR2 baseline
Use cold (2K) quadrupoles in the cryomodules, independently aligned from the cavities (+: minimise cold/warm transitions and maximize real estate gradient, TESLA experience, large aperture).
Use cryomodules of maximum length (between 10 and 15 m), containing n cavities and (n+1) quadrupoles. Diagnostics, steering etc. between cryomodules.
The length of the cavities should be limited by fabrication and handling considerations. The proposed number of cells per cavity is therefore 5, 6 and 7 for the three sections.
2 MW max power /coupler
standardisation of the design after 2 GeV

## Slide 15: CDR2 parameters
Ion species | H- | 
Kinetic energy | 3.5 | GeV
Mean current during the pulse | 40 (30 ?) | mA
Mean beam power | 4 | MW
Pulse repetition rate | 50 | Hz
Pulse duration | 0.57 (0.76 ?) | ms
Bunch frequency | 352.2 | MHz
Duty cycle during the pulse | 62 (5/8) | %
rms transverse emittances | 0.4 |  mm mrad
Longitudinal rms emittance | 0.3 |  deg MeV

## Slide 16: CDR2 block diagrams
SPL2 : 0 to 3.5 GeV in 450 meters

## Slide 17: why not 704 from the start ?
acceptance at 100kV 700 MHz too small
focusing from the RFQ too weak
Drift tube linac miniature dimensions
90 MeV is an optimal energy for the frequency jump

## Slide 18: why not higher than 704 after few GeV?
frequency jump needs longitudinal re-matching, i.e. lower synchronous phase
Phase profile in SC LINAC at one single frequency
Phase profile in SC LINAC with frequency jump

## Slide 19
1 frequency (MHz) | 2 frequency (MHz) | 3 frequency (MHz) | Length (m) | Nb of cavity
704 | 704 |  | 410 (ESS) | 222
704 | 704 |  | 407 | 219
704 | 704 | 704 | 336 | 129
704 | 704 | 1056 | 339 | 156
704 | 1056 |  | 382 | 177
704 | 1056 | 1056 | 345 | 154
1056 | 1056 |  | 390 | 189
1056 | 1056 | 1056 | 362 | 173
1056 | 1056 | 1408 | 363 | 187
1056 | 1408 | 1408 | 369 | 194
704 | 1056 | 1408 | 339 | 168
preliminary optimisation
by R. Duperrier, CEA Saclay

## Slide 20: gradient/power/length/cost
total cost in a linac is generally proportional to length
reliability is increased if the system has less components and the components are standardized
the fact of having in house the 352 RF power source is out weighted by the gain in lenght and reliability.
352 bulk niobium cavity are not a good economical choice
we can’t reach above 2.2 GeV by re-using the LEP klystrons

## Slide 21: energy and synergy
SPL must be a multi-user facility. Each user has a specific request on intensity/beam power/energy. Whilst intensity and beam power can be easily varied within the same machine (change of source current, change of duty cycle) the choice of the final energy must be such as to accommodate the max number of possible users.

## Slide 22: energy and synergy
potential users :
  Eurisol
  betabeam
  superbeam
  neutrino factory
  CERN proton complex
1-2 GeV 5 MW
above 2 GeV 4 MW
200 MeV, above 2 GeV
3.5 GeV 4 MW

## Slide 23: CDR2 contributors
The SPL study group at CERN
CEA Saclay and INFN Milano
HIPPI
ISTC collaboration with Russian laboratories and nuclear cities

## Slide 24: 3-stage approach
Stage 1: 3 MeV test place
   development and test of linac equipment, beam characterization
Stage 2: Linac4
  New linac replacing the present injector of the PS Booster (Linac2)
  Front-end of the future SPL
   improvement of the beams for physics (higher performance and easier operation for LHC, ISOLDE etc.)
Stage 3: SPL
  New injector for the PS, replacing the PS Booster
  New physics experiments using a high proton flux
   improvement of the beams for physics and possibility of new experiments

## Slide 25: Global planning
3 MeV test place ready
Linac4 approval
SPL approval
RF tests in SM 18 of prototype structures* for Linac4
CDR 2

## Slide 26: Conclusions
CDR2
expected by the end of 2005
cointaining a feasibility study for a 3.5 GeV Superconducting H- LINAC based on 700 MHz cavities
results of the evolution of CDR1 with contribution from CEA-Saclay, INFN Milano, HIPPI, ISTC ....

## Slide 27: Benefits of the SPL
Performance upgrade of LHC
  much higher beam brightness: necessary step towards an increased luminosity
  easier operation & higher reliability
Second Generation Radio-active Ion Beam Facility (EURISOL):
  proton beam power x 1000
  flux of radio-active ions x 1000
Neutrino physics
  “super-beam (10 x beam power foreseen for the “CERN Neutrino to Gran Sasso” experiment)
  “beta-beam”
  Neutrino factory
High energy physics with fixed targets
  Easier operation, higher reliability & higher performance of the injector complex
The beam from a
single SPL can be
time-shared and
satisfy
quasi-simultaneously
all these needs

## Slide 28: Stages
Three stages are planned:
Stage 1: 3 MeV test place
   development and test of linac equipment, beam characterization
Stage 2: Linac4
  New linac replacing the present injector of the PS Booster (Linac2)
  Front-end of the future SPL
   improvement of the beams for physics (higher performance and easier operation for LHC, ISOLDE etc.)
Stage 3: SPL
  New injector for the PS, replacing the PS Booster
  New physics experiments using a high proton flux
   improvement of the beams for physics and possibility of new experiments

## Slide 29: SPL beam time structure (CDR 1)
Fine time structure
(within pulse)
Macro time structure