## Slide 1: Plans towards the final power supply
M. Omeich SERA
J.E Campagne

## Slide 2
mid-June 03: « cahier des clauses techniques particulières de l’alimentation pulsée de la corne de Neutrino » official document written by M. Omeich (13pages):
  This describes the different technical characteristics required at that time both for the power supply and the switches,
  The contract between the factory(ies) and LAL and CERN
1st industrial price feed back:
  Main power supply (7kV/130A): HAZEMEYER co.: ~ 160k€
  Swithes (300kA/100s/50Hz): ABB co: ~ 3x2x50k€* = 300k€
A solution exists for ~ 460k€ (700kCH)
Industrial solution…
*: factor 2 for # of switches, factor 3 for 1Hz -> 50Hz

## Slide 3
We think that we have time to do some R&D to decrease the price (certainly the study is included the price…).
F. Völker has a nice setup at CERN that he has pushed to 100kA/1Hz
Power
Sw1 (50kA)
Sw2 (50kA)
Horn
With also the
. 1500F load
. Energy recovery circuit
We propose to continue the R&D
by x3 on each branch the number
of elements and change the power
if needed to reach 300kA/1Hz
R&D side

## Slide 4: CERN electrical circuit

## Slide 5: In a dream world…
We wish to transfert at LAL:
  F. Völker’s present setup (power supply?, switches, load, energy recovery circuit, cables…)
  and the Horn prototype
as soon as CERN group agrees that we can do it.
If Ok
  we will buy the same « semi-conductor » elements used presently to increase step by step from 100kA to 300kA (cost? cf. F. Völker)
  If needed we will increase the main power supply (present 3kV/10A ?)

## Slide 6
Then, we can experience what happens during this current increase on both sides:
  Power supply side: to qualify the switches and the schema in the perspective either to do the assembly at home either to negotiate the price with company…
  Horn side: to perform some strain measurements at higher current even if
    it may be already experienced with CNGS + F. Völker power supplies
    The Horn prototype design is not the final one (see. S. Wallon/A. Cazes)
Prepare ourselves for the next Horn prototype