## Slide 1: Calibration tools for water Cherenkov detector
Shoei NAKAYAMA (ICRR)
Aug 26, 2004 @ T2K collab. meeting

## Slide 2: Current K2K-1kt calibration tools

## Slide 3: Possible improvement
Laser ball (T calib.)
  more point-like light source
  more precise location
  various positions (not only at center)
Xe ball (Q calib.)
  more uniform light source
  more precise location
  various positions (not only at center)
Laser injector (light scattering calib.)
  various positions, directions, and wave-lengths (same as SK)
Cosmic ray pipe (vertex calib.)  later

## Slide 4: Dominant systematic errors
Fiducial volume (vertex fitter)
  in  disappearance analysis
  the number of  events is important
Ring counting
  In  disappearance
  in e appearance search
  the number of BG events to e signals, 1ring 0 events, strongly depends on the ring counting.

## Slide 5: Fiducial volume calibration
Calibration source :
   events ? cosmic  events ?
cosmic 
-induced
Cosmic  events have different event topologies from
those of neutrino events.  difficult to use…

## Slide 6: Idea for fiducial volume calib. (option1)
a black wall (curtain) + XY-segmented  detector
Black curtain
XY 2layerd, SciBar type, 3mx3m
2km WC detector
(side view)
The location of the curtain determines vertex Z.
Vertex X and Y are measured by the SciBar sheet detector.

## Slide 7: Idea for fiducial volume calib. (option1, cont’d)
stretch a vinyl black sheet using hooks on the detector wall during water supply or during water draining.
200 scintillator bars. (3cm width, 100 horizontal, 100 vertical)
assemble inside the tank after draining the detector water during beam-off periods. (construct a support frame and arrange each part)
water-proof each part.
take data in a few Z positions.

## Slide 8: Statistical requirement (option1)
event rate of opt1 =~ 1/5 x event rate of  int. in 100t fid.
=~ 0.02 ev / spill (wall position +300cm)
  estimated by MC.
  neglecting inefficiency in trigger condition and event selection.
difference in vertex shift towards Z direction between data and MC should be below 8cm(=800cmx1%) to achieve 1% systematic error.
 statistical error on the peak position in the Z distribution of
calibration data, / sqrt(N), should be below 8mm. (safety factor 5)
 N = 1400 ev (assuming vertex resolution  ~ 30cm)
 t = 1400 / 0.02 ~ 70000spills ~ 3days (@+300cm)
4.5days (@-100cm), 6days (@-500cm)  total 2weeks
statistical error on the X and Y position for this amount of calibration data  10cm/sqrt(1400) =~ 3mm  (2000+3)**2 / 2000**2 ~ 0.3%

## Slide 9
D. Casper
PMTs at the up- and down-stream fringes to identify event occurred in the Fid Vol.

Ch light should be detected

Ch light should not be detected
Idea for fiducial volume calib. (option2)

## Slide 10
Idea for fiducial volume calib. (option3)
E. Kearns

## Slide 11: Idea for ring counting calib.
Using fake Cherenkov-light generators is one possibility.
  Use the same system in 2km and SK.
     compare their responses
light source
diffuser cones
want to produce
fake e-like rings
The relative light strength and
the opening angle between the two cones
should be changeable.
Need to be
checked with
existing detectors.

## Slide 12: Summary
The 2km WC detector should have much better calibration tools than K2K-1kt currently has.
Fiducial volume calibration :
  We have some conceptual ideas.
  Simulation studies are needed.
Ring counting calibration :
  Cherenkov ring simulator is only one possibility at present.