## Slide 1
SINGLE-CHIP REAL-TIME DUAL BEAM FORMER WITH CORRELATION CAPABILITIES AT NRT
1 Virtex-5 FXT 100 FPGA/KIT ML523
12 twin Channels for FAN (but 24 complex gain sets), 24 (and later 32) channels for BAO cylinders
Full rate dual beam-forming for trigger ~30KHz
Addition from 2 to 65536 dual square-modules
Correlation : Visibility of only one channel pair at the same time <=> full rate with effective trigger 390Hz for 78 visibilities (12 channels) => Source tracking
Results on CasA transit
Results on 3c123 transit

## Slide 2
COMPUTATION OF THE VISIBILITIES WITH THE SAME FPGA AND ANOTHER FIRMWARE
Virtex 5 FxT 100 has 256 multipliers and 16 GtX transceivers : #16 at half rate
: #32 at 1/8 rate
*KIT Virtex-6 ML623** (LXT 240) has 768 multipliers and 24 GTX transceivers = 48 channels of ADC board, and can perform full-rate correlation at #16.
** $ 4995
N channels : N(N+1)/2 elements in the visibility matrix => 2 multipliers on the diagonal + 4 multipliers on the other parts = 2N2 multipliers
#12 channels => 288 multipliers
#16 channels => 512 multipliers
#24 channels => 1152 multipliers
#32 channels=> 2048 multipliers

## Slide 3
COMPUTATION OF THE VISIBILITIES WITH THE NEW VC707 VIRTEX-7 BOARD
UNIBOARD
10,304 multiplieurs
16x 10GbPS Rx+Tx (SFP)
Visi 70 canaux /coup horloge
(10304/2)1/2
VC707
2800 multiplieurs
16x 10GbPS Rx+Tx (FMC)
Visi 37 canaux /coup horloge
(2800/2)1/2

## Slide 4
CLOCK DISTRIBUTION (DISTCLK)
DISTCLK (emitter)
Control by external software
External 10MHz Reference Clock
DISTCLK (receiver)
8x RJ 45 Clock & command for 8 ADC boards
2x differential clocks for RF mixer
DISTCLK (receiver)
8x RJ 45 Clock & command for 8 ADC boards
2x differential clocks for RF mixer

## Slide 5
ACTIONS A VENIR
CORRELATEUR
  Nançay
    Visibilités en poursuite
    Gains obtenus par les visibilités du corrélateur
    Dual beam avec ces gains en transit et/ou poursuite
    Papier Real-Time 2012 à Berkeley (si accepté)
DISTCLK
  Mise au point routines de commande
  Simplification du code C du FPGA
  Mise au point de la carte réceptrice pour traitement de l'horloge fibre encodée
Stagiaire
AUTRE
  Automatisation Acq LAL/Corrélateur/DISTCLK/Chariot
  Amelioration du firmware du FPGA corrélateur
    RAZ individuel de chaque MGT
    Monitoring de l’alignement, lock PLLs… sur chaque canal.