## Slide 1: PAON project
J.E Campagne
LAL
17/5/2012
PAON: Paraboles A l’Observatoire de Nançay

## Slide 2: Organisation
Scientific Concil: R.Ansari (LAL), Ch. Magneville (CEA/Irfu), J.M.Martin (Obs. Paris/Meudon)
  + 6 other members
2 co-PI: J.E Campagne (LAL) & J.M.M
2 Project Ingeeniers:
  D. Charlet (LAL): Electronics & software
  F. Rigaud (Obs. Paris/Meudon): Mechanics & Nancay implantation

## Slide 3: Why Nançay (reminder)
150 ha of free field dedicated since the 50’ to radioastronomy
Close to Orsay ~ 2h drive dist.
Existing local infrastructure
Protected bandwidth [1400-1427]Mhz
Since 2008: BAORadio electronics at the focal plane of the NRT with 2 programs:
  Focal Array @ Nançay (FAN)
  HI-Cluster @ Nançay

## Slide 4: Budget from recent Scientific Committee @ Obs. Paris & LAL
LAL: 23k€
  Dishes, mounts, System control, DAQ PCs, cables
Obs. Paris/Meudon: 13k€
  Feed, dish-feed adaptation & Nançay infra.
CEA/Irfu: few k€
  LNA
~40k€

## Slide 5: PAON phases
PAON-2 (2012): validation phase
  2 Dishes  3m (RF Hamdesign)
  Elevation only manual
  Dedicated feed 1250-1500 MHz with LNA homemade
  Existing BAORadio electronics: 2 polarizations/dish
PAON-4 (2013): observation phase
  4 dishes in remote control
Goals: Beam, Noise, Cross-talk, Transit observation of fringes

## Slide 6: BAOradio existing chain (32 channels)
AEM : Analog Electronic Module ( Amplification, filtering, frequency shifter)
DCLK : Clock and trigger distribution system
DFS : Digitizer Frequency Separator (ADC-Board) 4 channel, 500 MHz sampling, with on the fly FFT capability, dual high speed optical data transfer
PDR : PCI-Express data reception module

## Slide 7: Some recent realizations…
X2/feed
RF-HAMDesign
Meudon/Nançay

## Slide 8
Frame for feed position commissioning
Fiber glass bars
Meudon

## Slide 9: Feed & dish simul.
8 Glass fiber bars
Dish+Feed only
Nançay

## Slide 10: Site considerations
Electromagnetic compatibility is a real matter of concern:
  The present basic mount is not useable for debugging phase (too noisy) => manual elevation positioning is foreseen (Ok)
  The DAQ electronics should be shielded too:
    PAON ask recently to be housed in the EMBRACE special container
PAON location is under discussion

## Slide 11: PAON location near EMBRACE
Design F. Rigaud (Meudon)
The special container

## Slide 12: Test of transit observation PAON-2

## Slide 13: PAON-2 to PAON-4
What was foreseen : Use 4 dishes 5m 
    in project @ RF-HAMdesign since Jan. 2011 4.5m in light material. But they have resigned April 2012 due to market considerations: ie. they have a lot of demands for <=3m and very few for >3m dishes
    Other manufacturers can provide larger dishes but either with poor mechanical characteristics either with very heavy dishes (>300kg) although well machined (eg. ComStar)
    Investigation for home made dishes in Meudon
In standby for the moment

## Slide 14: PAON-2 to PAON-4
Alternative: Use 6 dishes 3m 
  This is manageable but only ~40m2
  (compared to 70m2 with four 5m-dishes)
Objective: perform long term observation (several months) to show the stability of the whole BAORadio system:
    Fringes seen at Pittsburg up to 32-channels during small data taking
    Long term stability shown with single channel during the HI-cluster program at Nançay

## Slide 15: HI-Clusters stability
6 months of data taking (4h On source, eff. 30% DAQ)
Although we have identified many RFIs and 2 spectra modulations.